## Slide 1
Interference and Fourier Transform Spectroscopy
  Coherence and Interference
  Interferometry and Interferograms
  Fourier components
      time-dependence of a signal
      resolution
  Fourier Transform Spectroscopy
      Advantages
      Spectrometers
  Conclusions
Notes: Title and presentation

## Slide 2
Phase and Amplitude
Any oscillating quantity A(t) = Aocos (t-k.r+) (for electro-magnetic waves the electric field vector and the magnetic field vector) is characterized by :
  the oscillation frequency 
  the wavelength, /|k| v/
Once the frequency has been fixed (monochromatic wave) and the velocity of propagation “v” is given
  the amplitude = the maximum value Ao
  the phase of the wave 
Of course, the phase definition related to a reference e.g. a second component of the same beam

## Slide 3
The two wave components (A1,A2) recombine at the exit of the interferometer and sum their instantaneous amplitudes: the eventual phase delay of one wave with respect to the other must be taken into account.
Let us consider a wave travelling from a source S to a beam splitter B
S
B
A1
A2
MIRROR 1
MIRROR 2

## Slide 4: Phase modulation : Interferogram

=
=
A
The final amplitude of the out-coming wave is then modulated by the relative phase shift of the two wave components.
When the phase shift (or the delay) of one of the compo-nents is changed (e.g.: by changing the optical path, moving a mirror or intro-ducing a different medium) the amplitude, and then the intensity of the outcoming wave is correspondingly changed.

## Slide 5: Interferogram

## Slide 6: Interferogram
Each component with frequency  and wavevector k = /c is then modulated by the spatial delay z;
The whole beam can be described by the sum (the integral) of all the components;
By considering the intensity of each component (and of the whole beam) one is obtaining a sum of a constant term and a modulated one.

## Slide 7: Interferogram
When the delay z is described as a continuous, linear function of time, one can show that the resulting intensity is also time dependent and corresponds to the Fourier transform of its spectral function.

## Slide 8: Interferogram
The function of time (interferogram) obtained is different depending on the spectral content of the light beam:
A single frequency beam will be modulated as a continuous cosine function;
A spectrum extended over a frequency region will approximate a delta function (pinned at z=0) as better as the frequency region is larger.

## Slide 9: Interferogram and resolution


I()
I(t)
t


I()
I(t)
t

t=2/

## Slide 10: Interferogram and resolution
Problem: it is obviously impossible to measure an interferogram developing in time from - to .
What is then the effect of taking a limited portion of signal (let us say from t=- to t=)?
Answer: there is a kind of inverse symmetry between the two conjugated spaces. As shown in the pictures above, inasmuch a structure is narrow on one side, as much its transformed counterpart is extended.
This also means that we can only distinguish among different spectral components close one to the other if the correspon-ding interferogram is wide enough.
Resolution depends on the length of the interferogram

## Slide 11: Interferogram and resolution
As an example let us consider the interferogram obtained by the sum of two components at frequency 1 and 2, respectively. It will consist of the product of two cosine function: one of frequency [v(1+2)/2c] and the other one of frequency [v(1-2)/2c].
The first one is a rapidly varying function corresponding to the interferogram of a single component spectrum with an average frequency between 1 and 2.
In order to discriminate between 1 and 2 one has to wait a time corresponding to the period of the second, slowly varying function, which bring the information about the difference 1- 2.
+
=
| …. t = 4c/v(1-2) … |

## Slide 13: Resolution and Apodization
The truncation of the interferogram at the limits – and + can be viewed as the multiplication of the interferogram by a boxcar function having the same limits.
According to the convolution theorem and considering that the Fourier transform of a boxcar function is the sinc function, the resulting Fourier transform of the considered interferogram is the convolution of the Fourier transform of the whole spectrum with the sinc function with argument (t/).
Since the sinc function introduces some lobes in the spectra of narrow lines, it is sometimes preferred to multiply the interferogram by a function which reduces the intensity to zero at the limits – and +. This can be a triangular function, or an exponential decay, or a combination of function. The effect is the reduction of the lobes, payed by a loss of resolution.
Such an operation is called Apodization.

## Slide 16: The convolution theorem
La trasformata di Fouroier della convoluzione di 2 funzioni è uguale al prodotto delle trasformate di Fourier delle 2 funzioni

## Slide 20: DFFT Discrete Fast Fourier Transform
The need of a discrete sampling of the interferogram data allows the use of a computer and fast algoritmes to make the transformation.
Nevertheless the discrete character of the data introduces some further problems and requires some caution in producing and evaluating the results.

## Slide 21: DFFT Aliasing
The sampling theorem says that the sampling frequency must be the double of the largest frequency max of the signal. That means that, in order to avoid spurious contributions (aliasing), one needs some kind of low pass filter (optical or electrical) which cut the spectrum above max .
Due to the discrete character of the sum, the Fourier transformed function results to be a symmetrical and periodic function in the frequency space, with period 1/2max . (this is way a component with frequency larger than max should be folded and superimposed to the lower frequencies, leading to a wrong spectrum)

## Slide 22: Phase correction
All the components of an interferometer introduce, in general, both an intensity correction and a phase contribution to the interference beam. The amplitude (intensity) effects are similar to the ones introduced by any optical device in a spectroscopic experiment, and call for the need of a reference measurement.
The phase effects are peculiar of the use of an interferometer. In general, the phase shift introduced by the optics (mirrors, beam splitter, retardation plates) is a function of the wavelenght and of the experimental geometry (since one has to do with several different optical paths when the light beam is not perfectly collimated) and is adding to the modulation shift intentionally created in the experiment.
The effect of such a situation is that each component is added to form the interferogram with a different phase shift; in other words, both cos- (symmetrical) and sin- (antisymmetrical) functions contribute to the interferogram. It means that both real- and imaginary- components are obtained after inverse FT.

## Slide 23: Phase correction
Since the experiment result is usually an intensity value, just the power spectrum is actually interesting. Nevertheless, the calculation of the phase correction is a necessary step in the process.
Phase spectrum is, in general, a slowly varying function of the frequency; then a low resolution evaluation is enough to have a good correction. Such a spectrum can be interpolated in order to be used for the correction of a high resolution spectrum.
This way of proceeding has two advantages:
  A more efficient averaging of the noise in the spectrum can be achieved using with respect to
  The possibility of dealing with an interferogram not symmetrically displaced around its maximum (which is the ordinary case in the experiments)

## Slide 24: How is Working a Fourier Transform Spectrometer

## Slide 25: Main features of a Fourier Transform Spectrometer
Besides the necessary lamp and detector, the key features of a FTIR instrument are:
  An interpherometer moving mirror whose position can be controlled to a high accuracy (usually such a control is obtained with the help of a laser);
  A sampling and acquisition system which allows to obtain the correct time dependence of the interferogram;
  An analysis system which can perform the FFT (fast Fourier Transformations) and correctly evaluate the corrections (intensity, phase and noise effects introduced by the experimental setup).

## Slide 26: Main features of a Fourier Transform Spectrometer
The interference signal of a laser beam colinear to the light path in the interferometer is used to control the position of the moving mirror with a precision of less than 1 nm;
The same interference fringes of the laser are used for the sampling of the data: according to the Nyquist theorem, one must sample the data at a frequency (at least) double of the maximum frequency of phase modulation;
An usual PC is nowadays enough to perform the mathemati-cal data treatment (and also to control the whole experiment)

## Slide 27: Advantages of FTIR Spectroscopy
The so-called Jaquinot advantage: there is no need of slits which limit the throughput of radiation, so one can have a large signal without affecting the resolution;
The Fellget (multiplex) advantage: the whole spectrum is obtained simultaneously for all the frequencies from a single interpherogram;
Because of the two features above, it is possible to obtain instruments with a much higher resolving power than in dispersive instruments, even when the beam energy is low;
Since mirror mouvements can be very fast (and/or very precise), time resolution is easily implemented.